## Slide 1
SSA CONNECTOR/CABLE STANDARDS CONNECTIONS AD HOC WG RECOMMENDATIONS
THE FOLLOWING CONTENT AND ORGANIZATION IS PROPOSED FOR SSA PH-1:
  EXTERNAL CONNECTIONS
    BULKHEAD RECEPTACLE WITH TRI-RETENTION (JACK SCREWS, SLIDELATCH JACK POST, DETENT)
    CABLE PLUG WITH EACH RETENTION METHOD SPECIFIED
    MATING CYCLES, RETENTION FORCES, CRITICAL INTERFACE DIMENSIONS AND TOLERANCES NECESSARY TO ENSURE INTERVENDOR MATABILITY
  INTERNAL CONNECTIONS
    4 BAY DEVICE CONNECTION
    POWER BAY CABLE CONNECTION
    OPTION BAY CABLE CONNECTION
    PORT BAY CABLE CONNECTION
    4 BAY BACKPLANE CONNECTION
    A SUBSET OF THE P1394 DOCUMENTATION REQUIRED FOR INTEROPERABILITY
X3T10.1 / 95A-146

## Slide 2
INTERNAL CONNECTIONS TO NON-DISK DEVICES (FOR EXAMPLE,CONTROLLERS)
  THE STANDARD WILL BE SILENT ON THIS ISSUE
INTERNAL CABLE
  THE INTERNAL CABLE MAY REQUIRE SHIELDING IN SOME IMPLEMENTATIONS TO MEET THE NORMATIVE REQUIREMENTS FOR AN SSA NODE -- THE USE OF SHIELDING IS OPTIONAL
  IF SHIELDING IS USED, THE SHIELD SHALL BE CONNECTED TO PIN 3 IN THE IN INTERNAL PORT BAY CONNECTOR WHICH IN TURN SHALL BE CONNECTED TO CHASSIS GROUND IN THE DEVICE
  PIN 4 IN THE INTERNAL PORT BAY CONNECTOR SHALL BE LOGIC GROUND AND SHALL NOT BE CONNECTED TO THE SHIELD IN THE INTERNAL CABLE ASSEMBLY
  IF THERE IS NO CHASSIS GROUND AVAILABLE IN THE DEVICE, THE SHIELD PIN (PIN 3) SHALL BE CONNECTED TO THE LOGIC GROUND ON THE DEVICE SIDE OF THE CONNECTOR
* “DEVICE” MEANS DISKS, CONTROLLERS, OR OTHER ENTITIES ACTING AS AN SSA NODE
SSA CONNECTOR/CABLE STANDARDS CONNECTIONS AD HOC WG RECOMMENDATIONS

## Slide 3
SSA CONNECTOR/CABLE STANDARDS CONNECTIONS AD HOC WG RECOMMENDATIONS
CABLE LINES
(LOOKING AT DEVICE END
OF UNMATED CONNECTOR)
DEVICE PIN FUNCTIONS
(LOOKING AT UNMATED CONNECTOR)