## Slide 1
MDSM Impedance Transfer Impedance

## Slide 2
MDSM Impedance
Measurement details , if not other specified
TDR Tektronic CSA803A
Chip resistor direct connected to pcb tails of external device connector .
External cable connector harnessed with 100mm Madison cable 6702 . 300mm of 50 Ohm cable connected between Madison cable and TDR
50 Ohm and Madison cable copper braid linked together
Differential signal applied
Measurement single ended
Cable on input side

## Slide 3
MDSM Impedance Measurement
Verify connector impedance at higher data rates for SSA PH2
Three different connector configurations tested .
  Standard harnessed
  PCB applied in the cable connector MDSM - 9SC
  Increased cable shielding inside shield can.

## Slide 4
imped5.tif
Actual data: 125 ps 56 / 89 Ohm 250 ps 65 / 82 Ohm 500 ps 78 / 72 Ohm 750 ps 77 / 74 Ohm
MDSM Impedance
80 Ohm
70 Ohm

## Slide 5
MDSM Impedance
Actual data: 125 ps 47 / 85 Ohm 250 ps 52 / 80 Ohm 500 ps 61 / 78 Ohm 750 ps 65 / 76 Ohm
impedpcb.tif
70 Ohm
80 Ohm

## Slide 6
MDSM Impedance
Actual data: 125 ps 54 / 81 Ohm 250 ps 63 / 77 Ohm 500 ps 69 / 77 Ohm 750 ps 71 / 77 Ohm
imped1.tif
70 Ohm
80 Ohm

## Slide 7
MDSM Impedance Measurement
Further investigations with an integrated pcb / termination methods are required to meet data rates higher than 40 MB/ s .
Standard harness meets SSA PH2 at rise times up to 500 ps .

## Slide 8
MDSM Transfer Impedance
Shielded against EMI / RFI
Exceeds shield effectiviness requirements as specified by X3T10.1 / 1145D rev.8a for SSA PHase 1

## Slide 9
MDSM Transfer Impedance
Transfer impedance curve marked at 750 MHz - 22 dB
Test method: Line injection method -tested at Bosch-ANT

## Slide 10
MDSM Transfer Impedance
Transfer Impedance MHz SSA PH1 MDSM Actual 10 - 56 dB 30 25 dB - Ohm 47 dB 159 16 dB - Ohm 34 dB 500 10 dB - Ohm 25 dB 750 - 22 dB 1 000 - 19 dB

## Slide 11
MDSM
MDSM -9PE-Z42 Shielded Device Connector with 90° PCB Tails

## Slide 12
MDSM
Shielded device connector MDSM-9PE with universal jackpost for wall thickness 0.060" (1.5mm)

## Slide 13
MDSM
MDSM -9SC-Z20/Z24/Z40 Shielded Cable Connector
Z40 = Long thumb screw

## Slide 14
MDSM
Positive quick latching retention method available : Push-Pull - Z24
Long thumb screw - Z40
Proven D - shape polarized interface
Intermateable with connectors according to MIL-C-83513

## Slide 15
MDSM
For technical and commercial support please contact :
  Product Manager Wolfgang Drichelt +49 7151 699 233 +49 7151 699 221 Fax Internet e-mail "101573.2601@Compuserve.com"
  Product Specialist Monica Roy +1 714 757 8472 +1 714 757 8303 Fax Internet e-mail "monicar@mailgw.cannon.itt.com"