## Slide 1
PCI to SSA Adapter
A single chip interface between PCI and Serial Storage Architecture
Adge Hawes, IBM Storage Subsystems
April 1996
Notes: IBM has long been the pioneer in bringing a much-needed serial interface to the world of Disk Drives and peripherals.
SSA is an open standard invented in IBM Havant in England. IBM has been designing SSA interfaces both for its own and other’s use since 1992.
In August 1995 IBM began shipping the 7133 SSA Disk Array, setting a new price/performance standard in Disk Arrays. The 7133 has become a runaway best seller.
The chip described in this presentation is the culmination of the SSA work undertaken at Havant, bringing together the perfect match of SSA and PCI, now the internal bus of choice in the server marketplace.

## Slide 2
SSA Overview
Serial Link for Disk Drives
  20MB/s full duplex link, 40MB/s new version,
  160MB/s throughput for dual-port
  4 wire/port (Rx and Tx, differential), 8B/10B code
  25 metres/link, fibre-optic extension to 2.4Km
String, Loop and Switch topology
128 byte frames, 8 byte overhead (6%)
  Special characters for control
Spatial Reuse for maximum performance
  SAT Algorithm for fairness and arbitration
ANSI Standardization, now shipping (IBM 7133).
Notes: SSA is a standard serial disk interface that boasts a total throughput of 160MB/s at 40MB/s per link.
Each link contains 4 wires, consisting of two differential pairs, transmit and receive. 25 metres of copper are supported, or 2.4Km with an optical extender.
Any network can be configured, with string, loop and switched network topologies all possible.
The basic unit is the frame of 128 bytes, with typically 8 bytes of overhead (Address, channel and CRC).
Spatial reuse, the beneficial property of a point-point topology that allows otherwise idle links to perform useful work is exploited by a fairness algorithm called SAT which maximizes the available throughput.
The SSA specification is open, being governed by the X3T10.1 committee of ANSI.
IBM has shipped over 200 Terabytes of SSA storage in the IBM 7133 disk subsystem, since late 1995.

## Slide 3
SSA Shared Storage Array
Work Station
Work Station
Work Station
Work Station
Notes: A typical SSA high availability disk array is shown. Each adapter normally controls its local storage array (shown in the same colour), and will provide the maximum performance, but under failure conditions can take on the control of other storage in the array, thus providing high availability.
Each adapter is a PCI adapter consisting of a single chip providing all the SSA control interface.

## Slide 4
Spatial Reuse
up to 40MB/s write
up to 40 MB/s read
up to 40 MB/s read
up to 40 MB/s write
PCI: 120MB/s sustained
Bandwidth available = 4x link bandwidth
Limitation of PCI and memory
Notes: Spatial Reuse is what sets SSA apart from other serial interfaces. The independent control of each link means that useful work can be performed on all links, even those that would normally be considered idle.
Thus the maximum bandwidth available to an SSA network (Web) is up to four times that afforded by a single link.

## Slide 5
XORing disks and RAID
1. Read old Data (OD)
2. Read old Parity (OP)
3. Write new data (ND)
4. Write new Parity = ND ⊕ OD ⊕ OP
XOR new with old Write new Data Send result XOR new Parity
RAID 5 write without XORing disks or Spatial Reuse:
RAID 5 write with XORing disks and Spatial Reuse:
Notes: RAID (Redundant Array of Independent Disks) is a common technique available today to provide fault tolerant disk arrays. Each Data element that is written is part contributor to a “parity” element that forms the redundancy of the array.
If a disk drive should fail (as reported by its internal electronics), the missing data can be reconstructed in its entirety by reference to the surviving data and the parity.
Drives that can perform the XOR function, in conjunction with Spatial Reuse offered by SSA, offer at least a four fold improvement in RAID 5 write performance - traditionally the slowest component of the highly dependable RAID regime.
Spatial Reuse means that the parity data can traverse the array on links that would otherwise be unused during RAID 5 writes, improving the efficiency of the operation.

## Slide 6
SSA Traffic Flow
All frames go through frame buffers
“Through” frames - decrement address and pass on
Address=0: Data for this node
Inbound data for this adapter - must be captured and passed to the correct DMA channel on PCI
Outbound data from this adapter - must be fetched from the correct DMA channel in PCI memory and inserted into output stream.
Flag
Addr/chnl
Data (128 bytes)
CRC
Flag
Addr/chnl
Data (128 bytes)
CRC
3.4 µS
Notes: SSA traffic consists of random frames of 128 bytes. The problem faced by an SSA adapter is that it has to respond quickly to the demands of the SSA traffic.
Each frame that arrives on an SSA inbound port is either destined for this adapter or a “through” frame. Through frames must be passed on without delay. Frames for this adapter (designated by a ‘0’ address component) must be directed to the correct slot in PCI memory. This slot is indicated by the current state of the DMA channel in the chip, which in turn is selected by the ‘Channel’ component of the SSA Address.
If the adapter is currently wishing to originate frames, it must decide which channel to service and fetch that frame from PCI memory. Then it may (subject to the SAT rules) insert that frame into its output stream.

## Slide 7
“Laredo”
40/20 MB/s Dual-Port SSA
PCI 2.1 compliant
64-bit Addressing
15 DMA Channels/port
Internal Sequencer
  50MHz, 32-bit
  448x32 RAM
External ROM/RAM
3.3v CMOS.
FIFO/ byte
steer
SSA I/F
Port 2
SSA I/F
Port 1
Frame buffers
Control Store
Sequencer
PCI I/F
Ext mem
PCI
SSA
Notes: The chip that IBM is designing to perform the PCI to SSA function is codenamed “Laredo”. It will support both 20 and 40MB/s SSA operation. Each port can support 15 concurrent DMA channels; in other words 15 concurrent read or write operations can be in process per port at any one time.
All Laredo operations are controlled by an internal “Sequencer”, which involves itself with the day-to-day running of the chip and the processing of external commands. Also, scatter-gather operations (fragmented PCI memory chunks) are handled by the Sequencer.
There is limited internal memory for Sequencer Control Store and DMA channels, but this can be extended by the addition of external ROM or RAM. Up to 1MByte of external memory may be attached.

## Slide 8
SSA/PCI speed matching
120MB/s memory bandwidth available
FIFO allows 132MB/s burst for 128 bytes
Byte steering allows unaligned transfers
No wait states.
Frame Buffers
8x32 FIFO
40MB/s SSA
Byte Steering
40MB/s SSA
PCI Interface
PCI
120MB/s
Filling FIFO
PCI Burst Writes
FIFO Depth
Pre-fill
Fill from mem - empty to PCI
Empty
0
1
2
3
4
5
6
7
8
Notes: The PCI interface is provided by a macro designed by IBM’s Haifa design centre in Israel. This is a fully PCI 2.1 compliant design that is highly efficient in its use of PCI resources. This is achieved by depending on a guaranteed source of data for a PCI burst transaction - this means that the PCI cycles will not generate wait states. In contrast, other PCI designs insert wait states to match PCI to slower internal operations, denying those cycles to other PCI agents.
The peak bandwidth demanded by the macro could, of course, be 132MB/s. The Laredo Frame Buffers are able to supply 120MB/s, so an 8x32 FIFO is used to supply the buffer necessary to sustain the 132MB/s for the duration of the 128 byte (32 word) transfer.
A Byte Steerer allows PCI and SSA 32-bit words to be misaligned. The logic will reorganize the words, and if necessary insert an extra cycle.

## Slide 9
A Channel Descriptor Block is fetched for each frame, in or out
Inbound frames:
  Channel component directs DMA engine
  128 bytes are posted into PCI memory
Outbound frames:
  Arbitration/Fairness selects channel to be serviced
  More than one frame may be transmitted for channel
  SAT Algorithm governs origination
Scatter-gather boundaries handled by Sequencer
Control Blocks - access to PCI by Sequencer.
DMA
Count
PCI Address
SSA Address
Notes: The DMA hardware controls the direction of data between PCI and the SSA frames. Each channel is allotted a Channel Descriptor, which describes the PCI address, SSA details and Byte Count of the transaction. CD’s are stored in Laredo’s on-chip Control Store, and are fetched when either an inbound frame is to be directed, or an outbound channel needs to be serviced.
For transactions continuing beyond a contiguous PCI block of memory, the sequencer reloads the DMA CD at every Scatter-Gather boundary.
Control Blocks are those areas of PCI memory used by the Sequencer, and are transferred only between PCI and Laredo.

## Slide 10
PCI Communications
Sequencer provides configuration address space
External ROM/RAM for extra configuration and PCI BIOS
Transactions via chained tag blocks in PCI memory
PCI Address
Command
Command
Notes: PCI Configuration information is stored in the Sequencer’s Control Store, or in external memory if fitted. The external memory can also provide space for PCI BIOS, and is mapped into the PCI’s address space in the PCI convention.
Commands are sent to the Sequencer by means of chained Tag Blocks in PCI memory. Information about the location of the first command is posted to the Sequencer, thereafter the sequencer fetches command blocks from PCI memory, and posts results in PCI memory in a similar fashion.
This technique requires the minimum of precious internal chip storage.

## Slide 11
Conclusion
Single-chip PCI-SSA Interface, PCI 2.1 compliant
40 and 20MB/s link operation
Programmable via on-chip Sequencer
Scatter-gather support for data transfer
Good PCI citizen - no wait states
External Memory Interface
Low cost CMOS.
Notes: This presentation has described “Laredo”, an IBM-designed PCI-SSA interface chip. The chip uses IBM’s 3 years of practical SSA experience to provide a highly efficient low cost single-chip PCI-SSA implementation.
The chip is notable for its state-of-the-art 40MB/s SSA support, programmable operations, and good “PCI citizenship”.
The chip is being used to further streamline the efficiency of SSA disk Array designs.