## Slide 1
Networking over SSA
Preliminary Study Report
Mark A. DeWilde

## Slide 2
Program Goals
Provide applications using existing networks to migrate transparently to SSA networking
Allow a single SSA adapter to support both storage and network I/O
Minimize overheads in protocol support and over the SSA web

## Slide 3
Approaches
A. Define a new TCP-like protocol to provide the same services to applications as TCP/IP and UDP/IP but without the overhead and functions redundant to SSA transport.
B. Alternately, define an efficient means to tunnel IP datagrams between SSA nodes adding minimal protocol to that imposed by TCP/IP and UDP/IP

## Slide 4
SSA-TCP PROTOCOL
Connection oriented service application interface consists of OPEN(), CLOSE(), SEND(), RECEIVE(), STATUS(), and ABORT() service calls, with asynchronous event notification to application.
Connectionless service application interface consists of SendTo(), ReceiveFrom() and CreateRcvPort() calls, with asynchronous event notifications.
Defines an interface with transport layer that cleanly divides the layers and permits other protocols to share transport managed resources.

## Slide 5
SSA-TCP Protocol (contd.)
Most header-resident protocol handshakes are converted to SMSs, 7 new SMS commands, 6 new reply SMSs. Use of SMSs replaces TCP header. IP header unnecessary with SSA Transport.
Handles connection loss and repathing/multipathing
8k transfer incurs 6%-9% total overhead
Transport interface could be made more generic for other serial transport layers.

## Slide 6
IP over SSA
Minimal preliminary work done to date, mostly exploring possible means to implement.
One approach is to create SMSs to perform the work of IP headers, similarly to SSA-TCP
Alternate approach is to use dedicated channels for IP data and embed socket information in headers of fixed length packets
Represents lower efficiency bandwidth usage of SSA, but much smaller software effort across multiple operating systems

## Slide 7
Current Program Status
SSA-TCP document ~75% complete, requires ~1 man-month to complete
SSA-IP document not started. Study needs ~1 m-m to complete and document another m-m
Pathlight is currently evaluating the need for networking over SSA and the priority for dedicating the resources

## Slide 8
Unresolved Issues
Microsoft and some other operating systems architectures do not permit the use of the same device by both storage and network drivers, making dual use difficult without “cheating” in hardware
Vendor-Unique or ANSI Standard ULP code?