## Slide 1: TSR step by step
Write Once versus Rewritable
## Permission is granted to members of INCITS, its technical
## committees and their associated task groups to reproduce
## this document for the purposes of INCITS standardization
## activities, provided this notice is included.

## Slide 2: Rewritable, PC data
1. Host issues WRITE command with TSR=1.
2. Drive shall write data and detect error (for instance with verify). If defective sectors are found, then drive shall register the address of the defective sectors.
3. If Drive report error, host shall get the defect status from the drive.
4. Host shall issue WRITE command with TSR=0 for defective sectors.
5. Drive writes the data and performs DM with linear replacement.

## Slide 3: Write-Once POW, PC data
1. Host issues WRITE command with TSR=1, non-POW.
2. Drive shall write data and detect error (for instance with verify). If defective sectors are found, then drive shall register the address of the defective sectors.
3. If Drive report error, host shall get the defect status from the drive.
4. Host shall issue WRITE command with TSR=1 for defective sectors.
5. Drive writes the data and performs DM with linear replacement.

## Slide 4: Rewritable and Write-Once, Video stream
1. Host issues WRITE12 command with TSR=1 and Streaming=1.
2. Drive shall write data and detect error (for instance with verify). If defective sectors are found, then drive shall register the address of the defective sectors.
3. If Drive report error, host shall get the defect status from the drive.
4. Host should issue WRITE12 command with TSR=1 and Streaming=1 to write video chunk at new position.
5. Go to step 2 until no defective sector is found.