## Slide 1
FAST 20 SCSI DEVICE CAPACITANCE VALUE
TWO VALUES FOR THE MAXIMUM CAPACITANCE AT THE FAST 20 DEVICE CONNECTOR ARE PRESENTLY UNDER DISCUSSION --- 20 pF AND 25 pF
THE 25 pF VALUE IS THE SAME AS FOR SCSI-2 AND SCSI-3 SPI: IT IS ALSO THE VALUE USED FOR ALL SINGLE ENDED FAST 20 TEST RESULTS TO DATE
THE 20 pF VALUE IS BEING CONSIDERED BECAUSE IT WILL GIVE MORE NOISE MARGIN IF ALL (OR MOST) DEVICES ON THE BUS USE IT
THERE IS SIGNIFICANT DISAGREEMENT WITHIN X3T10 ON THE VALUE TO BE USED FOR FAST 20
THIS IS THE ONLY AREA OF THE FAST 20 DRAFT SPECIFICATION WHERE ANY DISAGREEMENT PRESENTLY EXISTS

## Slide 2
SINCE ALL EXISTING SCSI-2 AND SPI DEVICES MUST MEET THE 25 pF VALUE ONE MAY CONFIGURE ANY SCSI SYSTEM USING THE PRESENT FAST 20 RULES WITHOUT REGARD FOR THE MIX OR PLACEMENT ON THE BUS
25 pF PRESERVES THE PRESENT COST STRUCTURE IN THE SILICON, BOARDS, AND SWITCHABLE TERMINATORS
ANY CHANGE FROM 25 pF WILL INVALIDATE THE PRESENT FAST 20 CONFIGURATION RULES
NOT ACCEPTING THE 25 pF VALUE WILL DELAY BOTH IMPLEMENTATIONS AND THE FORWARDING OF THE FAST 20 DOCUMENT
IT WILL REQUIRE LARGE DECREASES IN CAPACITANCE (PROBABLY TO AROUND 10 pF) TO ACHEIVE THE INCIDENT WAVE SWITCHING REQUIRED FOR LONGER BUS LENGTHS AND FULL SPI LEVEL DEVICE COUNTS
FAST 20 SCSI DEVICE CAPACITANCE VALUE
THE CASE FOR 25 pF

## Slide 3
20 pF WILL INCREASE THE NOISE MARGIN WITH THE PRESENT FAST 20 RULES
IT MAY BE POSSIBLE TO ACHEIVE MARGINAL INCREASES IN DEVICE COUNT FOR FAST 20 (KEEPING EVERYTHING ELSE AS IS)
20 pF ENCOURAGES ALL SCSI IMPLEMENTATIONS TO USE LOWER CAPACITANCE -- WHERE ADOPTED MORE ROBUST OPERATION IS EXPECTED
IF THE 20 pF VALUE IS REQUIRED, BACKWARDS COMPATIBILITY IS STILL MAINTAINED IF THE PRESENT FAST 20 CONFIGURATION RULES ARE USED
NEW, MORE RELAXED, CONFIGURATION RULES FOR FAST 20 MAY BE POSSIBLE
FAST 20 SCSI DEVICE CAPACITANCE VALUE
THE CASE FOR 20 pF

## Slide 4
SOME OPTIONS
ACCEPT THE 25 pF VALUE AND GET ON WITH FORWARDING THE DOCUMENT (AN ANNEX WILL EXPLAIN THE BENEFITS AND COMPLEXITIES OF USING LOWER VALUES)
AS ABOVE BUT WITH THE 20 pF VALUE INSTEAD OF THE 25 pF VALUE (NO OTHER WORDING CHANGES IN THE FAST 20 DOCUMENT) AND FORWARD THE DOCUMENT
ACCEPT THE 20 pF VALUE AND DEVELOP NEW CONFIGURATION RULES FOR PURE FAST 20 SYSTEMS
ACCEPT THE 20 pF VALUE AND DEVELOP NEW CONFIGURATION RULES FOR MIXED FAST 20 AND SCSI-2/SPI SYSTEMS