## Slide 1
ATA Command Queuing October 13, 1994
James McGrath
Systems Engineer
Strategic and Technical Marketing
Quantum phone: 408-894-4504
500 McCarthy Blvd fax: 408-894-6375
Milpitas, CA 95035 internet: JMCGRATH@QNTM.COM

## Slide 2
Document History
ATA Command Queuing
General Note: revisions are coming out fast, prompted by good feedback - do not consider things set in stone, give me feedback!
Revision 5: feedback from revision 4:
-- added note in slide 9 and appendix A to deal with HEAD OF QUEUE
-- made slide 16 consistent with 15 in use of lock and arbitration bits
Revision 4: first document for general distribution, targetted at the October 19 ATA-3 meeting. (October 13, 1994). This is an architectural overview, with some key decisions (e.g. how to pass the tag) and timing considerations still loosely defined. The key is to look at the forest first, then the trees.
Revision 2 and 3: incorporate private feedback from several companies. (October 11, 1994)
Revision 1: initial proposal (October 4 1994)

## Slide 3
Agenda
ATA Command Queuing
Why Command Queuing on AT Drives?
Why the Drive and not the Host?
IO Subsystem Constraints
Host Constraints
ATA is Simplier than SCSI Command Queuing
ATA Protocol Changes Needed for Command Queuing
Configuring the Host for Queuing
Queue Tags
Synchronizing the Host and the Devices
Implementing Locks (Host to Device)
Host Sending a Command to a Device
Arbitration Between Two Queuing Devices
Implementing Locks (Device to Host)
Status and PIO Data Transfers
DMA Data Transfers
Transfer Count
Error Recovery

## Slide 4
Why Command Queuing on AT Drives?
ATA Command Queuing
Goal is higher drive performance at little or no additional cost
-- SCSI workstation class drives have demonstrated up to a 2 fold improvement in random performance under heavy loads (e.g. 16 commands) at no incremental cost
Will a Queue of commands exist in PC systems?
-- A key enabler is a multi-threaded operating system (Windows 95, Windows NT, Unix, OS/2, etc...)
-- Multi-threaded applications must take advantage of the OS
-- Multi-tasking and workplace environment will generate more IOs
-- Performance gain will be workload dependent
-- Benchmarks will be adapted to show off queuing at its best
Although protocol needs to be defined now to allow for ASIC and device driver development, we do not see a market need until 1996 or beyond.

## Slide 5
Why the Drive and not the Host?
ATA Command Queuing
Source of Performance Gain Relative Drive Host
Importance Capable Capable
Access Time Reordering 1 Yes No
Seek Time Reordering 2 Yes Yes
Command Overhead Overlap 3 Yes No

## Slide 6
Why Overlap Commands Between Two Devices?
ATA Command Queuing
In a well balanced IO subsystem, twice the throughput can be achieved by overlapping command execution (e.g. a simple mirrored system).
When one device is very slow (e.g. CD-ROM, Tape), this allows some overlap of fast disk IO with slow device IO.

## Slide 7
IO Subsystem Constraints
ATA Command Queuing
The IO subsystem consists of the host and one or two devices sharing an IDE cable (secondary address/cables are just a duplicate IO subsystem, although the primary addresses are used as examples throughout).
A component (host, device) can be queuing capable or non-queuing capable (a legacy component).
A legacy host gets no benefit from queuing. Queuing devices must be able to function with a legacy host, so queuing devices must power up in a queuing disabled mode and have queuing enabled by the host.
The queuing protocol proposal is designed to address the case of a queuing host and one or two queuing devices.
With a queuing host and a legacy device, the host simply does not invoke queuing. With a mix of queueing and legacy devices, the host cannot overlap commands between devices. It must also inform the queuing device so it can work in a non-arbirtaration mode.
ATA and ATAPI should be able to mix on the same cable (at least as much as they can do today).
Although focused on ATA commands, this proposal also works for ATAPI.

## Slide 8
Host Constraints
ATA Command Queuing
Queuing is not designed to work directly on the ISA expansion bus - local bus only will be supported.
-- Current proposal should work on ISA expansion buses, but we may wish to simplify some of the protocol and violate this compatibility.
Host connection is via a bridge (which may be discrete or integrated into system hardware) connecting a dedicated ISA bus to PCI/VL-Bus/EISA/MCA/other.
Since bridges must be supported, bridge constraints must be taken into consideration:
-- Intel PCI bridge guidelines allow access only to 3F6 and the task file
-- PCI bridges are moving towards first party DMA, implying no CPU intervention for data transfer. Therefore all drive data transfer protocol must be simply enough to be handled by a bridge chip.
Changes requiring new host hardware is allowed if the cost is small.
Queued and non-queued commands cannot be mixed on the same device.

## Slide 9
ATA is Simpler than SCSI Command Queuing
ATA Command Queuing
ATA has only one initiator
-- Number of available queue slots always known
-- Error recovery can be simple
ATA has no command reordering restrictions
-- All commands are treated like SCSI SIMPLE queue tag commands - drive can freely reorder any commands it receives
-- To insure strict order of execution (ORDERED queue tag), the host does not queue the command until the drive is idle - and does not queue the following command until the first has completed.
-- Commands cannot jump the queue (HEAD OF QUEUE queue tag does not exist) - although resetting the device, executing a command, and re issuing the aborted commands can impose a priority (Charles has suggested a less brutal technique - see appendix A)
From the upper level of system software, ATA and SCSI command queuing appear to be identical.

## Slide 10
ATA Protocol Changes Needed for Command Queuing
ATA Command Queuing
A legacy (non-queuing capable) device can co-exist with a queueing device. While commands can be queued at the queuing device, commands cannot be overlapped between the two devices.
Host must be able to send, and the device receive, a command while the device is executing another command.
Commands queued or executing at the device must be uniquely identified so that data and status can be returned to the host in a different order than the commands were received by the device.
An arbitrating protocol for the ATA bus must be developed so that command execution can be overlapped between 2 queuing devices.
Any protocol must work equally well with PIO and DMA commands.
An error recovery procedure must be specified
Ability for the host to detect queuing capability, the maximum queue size, and the ability to activate and deactivate the queueing protocol

## Slide 11
Configuring the Host for Queuing
ATA Command Queuing
By default devices power up in a non-queuing mode.
The host can determine if queuing is supported, and the maximum size of the queue, by issuing the IDENTIFY DRIVE command to the device.
Queuing is enabled/disabled by using the SET FEATURES command.
Arbitration is enabled by writing a 1 to bit 15 of device control register 6 (3F6).
The host must keep track of devices with queuing enabled vs devices without queuing capability or those with queuing disabled.
Queuing and arbitration must be re enabled after a hardware reset.

## Slide 12
Queue Tags
ATA Command Queuing
The host assigns each command an ID number, a queue tag.
Queue tag values range from 0 to (maximum queue size - 1).
Queue tag values are re used as commands are completed.
Queue tags are passed between the host and the device via either:
-- the data fifo, or
-- the upper byte of 3F6 accessed as a word.
Which of the above to do is still to be decided - the final document will specify only one (there will be no options)

## Slide 13
Synchronizing the Host and the Devices
ATA Command Queuing
Today ATA does not provide a way to insure the host can access the task file and device control registers without device interference, and vica versa.
A new lock request/lock granted mechanism is provided to provide such exclusive access at critical points in the command queuing protocol.
While a device or the host is locked, it cannot modify the contents of the task file or device control registers with the following exceptions
-- The host can always write to the soft reset and interrupt control bits.
-- The locked device can always make new data available via the data fifo register.
-- The locked device can always modify a few status bits that are not latched (e.g. index).
A lock can be though of as a SCSI connection. Although you may think of the locking mechanism analogous to the SELECTION/RESELECTION mechanism of SCSI, note that a host always locks BOTH devices.

## Slide 14
Implementing Locks (Host to Device)
ATA Command Queuing
Host locking all devices
-- A host requests a lock by setting a bit in writing a word at 3F6 .
-- Device 1 grants a lock request by asserting PDIAG within 25 ns and holding it for a short period (e.g. 50 ns) to signal device 0. Device 0 grants the lock request allowing the host to read a 1 in the device’s lock granted bit when it reads a word at 3F6. The grant must be available immediately (e.g. within 50 ns of request), and implies that BOTH device 0 and 1 have granted the lock.
-- In systems with a single queuing device, then that device can grant the lock without coordinating with the other device. Devices can tell if they are in a single queuing environment if queuing and arbitration are enabled.
-- A host considers the lock to be granted if the lock granted bit is set.
-- A host can clear a lock explicitly by clearing a bit in writing to a word at 3F6, or implicitly by writing to the op code register in the task file.

## Slide 15
Implementing Locks (Host to Device)
ATA Command Queuing
AE
LRLC
Queue Tag (or Reserved)
3F6 word access
bit
15
bit
14
bit
13
bit
12
bit
11
bit
10
bit
9
bit
8
AE
LG
Queue Tag (or Reserved)
LG = lock granted for both devices
Host Write/Drive Read
Host Read/Drive Write
LRLC = 1 for requesting a lock, 0 for clearing a lock
AE = arbitration enabled
R
D#
D# = 0 or 1, used to indicate device requesting a lock

## Slide 16
Host Sending a Command to a Device
ATA Command Queuing
Host requests a lock from both devices
Lock granted?
Host issues command
Yes
No
Assume two devices with queuing enabled
Host writes a 1 to bit 14 of device control register 6 (3F6)
Host reads device control register 6 (3F6) and checks if bit 14 is set
Host writes the tag into the bits 13-8 of 3F6 or the data fifo, the rest of the task file as normal, and finally writes to the op code register. Locks are implicitly cleared when op code is written.
Host writes a 0 to bit 14 of device control register 6 (3F6) to clear any locks
Host is blocked from issuing the command

## Slide 17
Arbitration Between Two Queuing Devices
ATA Command Queuing
If a device wishes to generate an interrupt to the host for data or status transfer, or to have the DMA controller transfer data, then it must make sure the other device will not interfere.
A pre condition for this protocol is the host enabling arbitration by writing a 1 to the AE bit (bit 15 of device control register 6) when two queuing devices are detected. Otherwise a queuing device may always assume arbitration has been won.
When a device is not locked, it can modify its copy of the task file registers in preparation for arbitrating for the bus. If the host requests a lock during this time the device shall refuse to grant the lock.
Device 0 can generate a interrupt or assert DREQ as long as the device is not locked and PDIAG is not asserted by device 1. The device is said to have won arbitration.
Device 1 can generate an interrupt or assert DREQ as long as the device is not locked and PDIAG has been asserted by device 1 for 500 ns without Device 0 generating an interrupt or asserting DREQ. The device is said to have won arbitration.
Instead of using PDAIG, it is possible to use the data lines. In this case it must be clear that the host will not react to the arbitration sequence.

## Slide 18
Implementing Locks (Device to Host)
ATA Command Queuing
Device locking a host
-- A lock is requested by the device by asserting IRQ (status and PIO data) or asserting DREQ (DMA data). Note that no other device can conflict since this device has won arbitration.
-- A lock is granted by the host by using the same mechanism as getting a host to device lock (for status and PIO data) - the host requests a lock, and is immediately granted it by the devices. Another mechanism may be evolved. For DMA data, the lock is granted by the host asserting DACK.
-- The host clears the lock in the same way as clearing a host to device lock (for status and PIO data) - writing a 0 to bit 14 of 3F6. For DMA, the lock is cleared when both DREQ and DACK are deasserted.
-- The host or DMA controller can identify the command for which a lock is being requesting by examining bit 13 of device control register 6 (the device number, 0 or 1) and bits 12 to 8 of the same register (the queue tag). Alteratively this information may be stored in the first data word transferred from the data fifo.

## Slide 19
Status and PIO Data Transfers
ATA Command Queuing
Device wins arbitration and generates an interrupt, and the host establishes a lock
Host reads tag value
Host transfers data (if any), checks status, and clears lock
Host writes a 0 to bit 14 of device control register 6 (3F6) to clear the lock
Host reads from bits 13-8 of 3F6 or the data fifo register
Assume two devices with queuing enabled

## Slide 20
DMA Data Transfers
ATA Command Queuing
Device wins arbitration and asserts DREQ, requesting a lock
DMA controller asserts DACK, granting the lock
DMA controller reads device number and tag
Assume two devices with queuing enabled
DMA controller transfers data until DREQ or DACK is deasserted
Lock is cleared when both DREQ or DACK are deasserted

## Slide 21
Transfer Count
ATA Command Queuing
After reading the queue tag, the host may read a transfer count word from the device’s data fifo register.
This value indicates the number of words of data available from the device for immediate transfer (i.e. words of data in the device buffer) for reads. It indicates the number of words of space available in the device for immediate transfer (i.e. words of space in the device buffer) for writes.
For PIO commands, this value is 256 for backward compatibility, but allows a larger, variable number of words to be transferred at a time.
For DMA commands, this value may not indicate the length of the current DMA burst, but does limit the length of the burst.
The transfer count mechanism may not be needed, but may assist the host and DMA controller in making transfers more efficient.

## Slide 22
Error Recovery
ATA Command Queuing
Errors are reported in the STATUS register as usual.
The devices continue execution as normal when errors occur - there is no halting of the queue.
The host can always abort everything via a soft reset - all the commands are wiped clean.
Individual commands can be aborted by locking the devices and issuing a NOP to the same device/queue tag as the command to be aborted. The drive will return with ABORTED command status.
Since ATAPI allows the gathering of more extensive sense information via REQUEST SENSE, the device shall maintain sense data for each command, discarding it when the queue tag is re used by the host. The REQUEST SENSE command packet must specify the tag for which sense is requested (there are lots of reserved bytes).

## Slide 23
Appendix A: another way to do HEAD OF QUEUE
ATA Command Queuing
Commant from Charles Monia (SAM editor)
Just one comment on your ATA queuing slides. On pp 9, you suggest that simulating HOQ commands would require the host-resident SCSI emulation software to abort and reissue previously pending commands.
As I describe below, it is possible for the host to simulate the behavior for HOQ and all other command types without going to those lengths.
One way to do that is for the host to maintain a host-resident queue of pending commands, as your slide suggests. A command is unconditonally entered on this queue when it is received and remains there until completion. The host marks commands on the HR queue that have been passed to the drive.
If an ordered command arrives and the HR queue is empty, the ordered command is immediately forwarded to the drive. Otherwise, the pending command is placed on the HR queue and forwarded when all previous commands have ended.
If a Simple command arrives and there are no pending HOQ or Ordered commands, the Simple command is forwarded to the drive. Otherwise, it remains on the queue and is forwarded when all previous HOQ and ordered commands have ended.
If an HOQ command arrives, it is unconditionally forwarded to the drive.
Even though there's no way to for such a command to 'jump the line' of commands that have been forwarded, that is not an issue since commands previous to an HOQ command are allowed to complete before the HOQ command completes.
I assume in all these cases that an error condition unconditionally aborts all commands that have been passed to the drive. Since all such commands would still be in the HR queue, the host-resident emulation software could just restart them when the ACA is cleared.