## Slide 1
SCSI PnP Termination
Statements in SCSI PnP do not eliminate disabled terminators on devices
Introduction 3 #
  PnP SCSI simplifies termination by making proper termination a side effect of configuring the system. Termination is not included within SCSI peripheral devices; thus the confusion over the presence of a terminator and the possibility of excessive terminators are eliminated.

## Slide 2
SCSI PnP Termination
Section 6.2 Termination Requirements
  This section defines the requirements of the terminator and terminator power. Section 7 defines the location of terminators in system configurations.
  All terminators in PnP SCSI systems shall conform to the terminator requirements in the SCSI-3 Parallel Interface document. The terminators shall operate correctly over a TERMPWR voltage range of 4.0-5.25 Vdc. Regulated terminators are required. These are often referred to as alternative 2 or active terminators.
  The host and the peripheral sub-system shall provide terminator power (TERMPWR) to the SCSI bus. All terminators must be powered from the TERMPWR line(s) in the SCSI bus.

## Slide 3
SCSI PnP Termination
  Note - Exceptions may be necessary for battery operated devices and PCMCIA PC-Cards.
  Devices providing TERMPWR must provide a self-resetting device (e.g. positive-temperature-coefficient or circuit breaker device) to limit the maximum amount of current sourced instead of a fuse. Such a device opens the circuit when excessive current is drawn and closes the circuit when the device resets.