## Slide 1
SPIT Goals
Small High Density Connectors
  IO Connector, 16 bit Data Bus
  IO Connector, 32 Bit Data Bus
  Device Connector, 32 Bit Data Bus
3.3 Volt Termpwr
  3.3 Volt guide lines
  3-5.25 Volt Interoperability
FAST-40 RAID/Server Applications
  Single-ended restricted bus & Device capacitance
  Differential
Full Hot Plugging Devices-not just in the Annex

## Slide 2
SPIT Target
SPIT needs to track the performance of the systems
  64 bit processors Systems and PCs, video servers, RAIDs 20 to 160 megabyte/second transfer rates required.
  Disk Sizes 2, 4, 8, 10 Gigabyte drives announce now, SPIT should be targeted to the future 10 to 100 Gigabyte drives.
  Ease of use.
  Reliable small connectors and cables.
  Hot Swap - even for PCs, not just RAIDs and servers.

## Slide 3
32 AWG Wire Cable
TERMPWR Voltage Drop
  1 28 AWG 8 bit bus - 3 / 6 meters
  4 30 AWG 16 Bit bus - 3 / 6 meters
  6 32 AWG 16/32 Bit Bus 1.5 / 3 meters
    higher current - Far end current 18 Lines 0.5 Amps, 27 Lines 0.75 Amps, 45 Lines 1.25 Amps
  50 pin Connector resistance
  68 pin Connector resistance SPI/SPIT (Miniature)
  100+ pin Connector resistance