## Slide 1
Low Power SCSI for Laptops
Laptop computers need to limit the power for longer battery life.
  Battery power units may not be able to provide TERMPWR for the far end terminators.
  Battery power units may not be able to power the terminator inside in normal power mode when an external cable is attached.
High performance and low power must work together.
  Size TERMPWR fusing for the application, 1 Amp min for 8 bit bus and 1.5 Amp for 16 bit bus.
  Regulated terminators reduce the TERMPWR current.
  Low power mode for the terminators on short bus configurations, automatic termination current adjustment when external cables are added.
Page 1

## Slide 2
Low Power SCSI for Laptops
Power Down Modes required when the SCSI devices are not in use, this includes powering down the SCSI bus, Termination, and controllers.
  No device errors when the bus is powered down or hang conditions.
3.3 Volt operation compatible with 5.0 Volt devices.
  Termpwr 2.8 < 5.25 Volts to the terminators at the far end of the cable.
  Units may require TERMPWR to be supplied externally for the controller terminator to run in normal power mode versus low power mode when running the internal bus only.
Page 2