## Slide 1
3.3 Volt SCSI Termpwr
Page 1
3.3 Volts TERMPWR Source.
  3.3 Volts minus JEDEC tolerance is 3.0 Volts.
  3.3 Volt systems should connect to 5 Volt SCSI termpwr requiring a regulator for 2.8 to 5.25 Volt operation.
Unidirectional Circuit Breaker Required for less than 0.2 Volt drop.
  Section reference SPI 7.3 Add note Use a Unidirectional Circuit Breaker for 3.3 Volt systems.
  Circuit Breaker Maximum drop, 0.2 Volts under full load
  Cable drop 0.1 Volts with 1/2 load
  Terminator regulator drop less than 0.2 Volts, all lines 24 mA load.
Change from SPI Table 7 (add) 3.3 Volt Single-ended 2,90 VDC Min 5,25 VDC Max 1000 mA for 8 Data bit buses.
Change from SPI Table 7 (add) 3.3 Volt Single-ended 2,90 VDC Min 5,25 VDC Max 1500 mA for 16 Data bit buses.

## Slide 2
3.3 Volt Requires 2.8 Volt terminators at the far end or power from an other device.
  Standard termination requires at least 4.0 Volts.
  Not all 3.3 Volt systems can provide power for the far end terminator.
  3.3 Volt Terminators must work to 5.25 Volts.
  Addition Special Icons showing users the limitations instead of the symbols shown in SPI Annex H.
3.3 Volt Basics
Page 2
Circle/Slash used when Termpwr is not
adequate for the far end.

## Slide 3
Termination
Regulated Termination
  SCSI-3 SPI Maximum pull up current is 24 mA at 0.2V.
  SCSI-3 SPI minimum pull up voltage is 2.5 Volts.
Battery systems often require TERMPWR to be supplied externally.
  Termpwr could be from a 5.25 Volt source, which requires all 3.3 Volt systems to run with 2.7 to 5.25 Volt TERMPWR.
Change from SPI section to 7.1.1 3.3 Volt Systems the terminators must regulate with TERMPWR from 2,7 VDC to 5,25 VDC
The regulated terminators shall use source/sink regulators to reduce overshoot, high Active Negation Driver pull up voltage, and protect 3.3 Volt Logic.
High voltage clamp to protect logic 3.6 Volts (AMD)
Page 3

## Slide 4
3.3 Volt Logic Issues
Maximum SPI-LV bus Voltage, ViH
  3.6 Volts is the maximum recommended voltage for 3.3 Volt logic. The JEDEC standard is 3.3 Volts +/- 0.3 Volts.
  Some controllers may require clamping when connected to 5 volt SCSI units that drive signal lines above 3.6 Volts.
Standard meet current standard levels except ViH maximum
  There is not problem using the standard thresholds for 3.3 Volt logic. 2.0 Volts is the maximum high Threshold.
  Recommended termination reference voltage is 2.5 to 3.0 Volts.
  Maximum pull up current with Termpwr from 2.7 to 5.25 Volts is 24 mA at 0.2 Volts.
  Terminators should not source current when the line is over 3.24 Volts.
Page 4