## Slide 1
Differential SCSI

## Slide 2
Differential Driver Power vs VOD
Bias does not affect average power in driver appreciably
Integration requires about 50 mW avg per driver
Lower VCC and/or VOD are the only path(s) to power dissipation reduction and integration

## Slide 3
What is LVDS?
LVDS stands for Low-Voltage Differential Signaling and is fundamentally RS-422 with reduced output signal levels, receiver sensitivities, and ground potential differences. It has been and is being standardized in IEEE and EIA/TIA.

## Slide 4
LVDS

## Slide 5
LVDS
>1Gbps (theoretical)
100 Mbps to 10 m over UTP in Laboratory
Transmission line from the die on out
Compatible with 3 V- or 5 V-logic semiconductor processes allowing integration and reduction in skew.

## Slide 6
Problems solved

## Slide 7
Problems created
Point-to-point vs bus structure
  A multi-drop bus structure would require doubling the driver output currents (lowering the load impedance) of LVDS
  High-impedance driver output requirements
  Stubs and bus loading and noise margins
  Idle-line failsafe

## Slide 8
Problems created
Backward Compatibility
  Not even close to the +/-7V ground potential difference capability of RS-485
  RS-485 signal can be attenuated to interface to LVDS receiver
  LVDS signal should be detectable by most RS-485 receivers but not assured
  Idle-line failsafe is not compatible