## Slide 1
Steve Sicola Digital Equipment Corporation
Fault Tolerant Controller Configurations for SCSI

## Slide 2
Fault Tolerant Controller Configurations For SCSI
Overview
  Common Fault Tolerant Controller Configuration for SCSI Today
  Features and Drawbacks of Today’s Configurations
  What Metrics of Fault Tolerance are Important to Customers?
  Why Standardize Fault Tolerant Controller Configurations? How?
  Options for Standardization & Conclusions

## Slide 3
Common Fault Tolerant Controller Configurations For SCSI Today
Many System Customers today want high availability with their storage
Controllers are part of the system, and must be made highly available using redundancy techniques
Redudancy Techniques include:
  Active + Hot Standby...
  Active + Active...

## Slide 4
Common Fault Tolerant Controller Configurations For SCSI Today
A typical Fault Tolerant Controller Configuration:
A typical Dual Controller Configuration
with two Controllers sharing access to
attached devices, in this case with 3 buses
being shared between the controllers.
This definition does NOT specify how
the controllers are attached to the host
or to the devices with parallel SCSI buses
...
...

## Slide 5
Common Fault Tolerant Controller Configurations For SCSI Today
Fault Tolerant Controllers add new details to access of host data by:
  allowing varying attachement to the host computers
    with more than one host port per controller
    with controllers attached on different host buses

## Slide 6
Common Fault Tolerant Controller Configurations For SCSI Today
Fault Tolerant Controllers add new details to access of host data by:
  Allowing various types of access to devices
    by the shared topology to the devices between the controllers
    by use of protocol policies such as Reserve & Release in SCSI.

## Slide 7
Common Fault Tolerant Controller Configurations For SCSI Today
Fault Tolerant Controllers add new details to access of host data by:
  Allowing Failover of device control from a failed controller to the survivor
    without host operating system support
    with host operating system support
  Allowing Failback with and without host operating system support.

## Slide 8
Common Fault Tolerant Controller Configurations For SCSI Today
A block diagram of a controller incorporating all possible attributes:
...
...
Host Bus 1
Host Bus 2
2 Host Ports
per Controller
Shared device
ports
Controller A
Controller B
2 Host ports allows for:
a)hot/standby controller w/o host
b)active/active w/o host support
but w/one host port idle until
failover.
c0 active/active w/ host support
but with all ports active
Attachment two two different host
buses enhances system availability but REQUIRES host support

## Slide 9
Common Fault Tolerant Controller Configurations For SCSI Today
Current solutions in industry for the typical configurations shown include:
  Vendor Unique host operating system support for single port per controller and/or multi-host bus attachment (Failover can be manual or automatic)
  Target Failover with 2 host ports per controller (2nd idle until failover). Failback can be automatic or manual.
  Target Failover with one host port, assuming hardware can act as >1 target.

## Slide 10
Features and Drawbacks of Today’s Configurations
Features:
  Highly Available Storage achieved
  Single host port controllers with or without host support reduce product costs
  Multi-host port controllers without host OS support achieve redundancy more simply.

## Slide 11
Features and Drawbacks of Today’s Configurations
Drawbacks:
  Non-Standard Implementations leading to possible interoperability problems on different platforms in the same system.
  Cost
  Failvover Time is not bounded by several techniques used.
  Some techniques used don’t adequately abort I/O’s on failed controllers.

## Slide 12
What Metrics of Fault Tolerance are Important to Customers?
Active-Active Configurations to achieve greater availability with their overall system/cluster, as well as performance of two controllers accessing shared data.
Failover/Failback time is critical in production environments.
They want it for free...

## Slide 13
Why Standardize Fault Tolerant Configurations in SCSI?
To Reduce the cost of Solutions
Because of the convergence of standards on many different interconnects that will have SCSI RAID controllers (FibreChannel, SSA, FAST 20 SCSI) coupled with customer desires of fault tolerance & interoperability with all their system boxes/software.

## Slide 14
Why Standardize Fault Tolerant Configurations in SCSI? How?
To Generalize the number of controllers in a fault tolerance configuration as well as the type of access allowed by hosts
Increase speed of failover from current techniques
Generalize the possible system topologies supported in simple terms

## Slide 15
Why Standardize Fault Tolerant Configurations in SCSI? How?
HOW:
Support in SCSI for ‘Registration’ of multi-controller configurations sharing device access. This would be contained within ‘conspiring’ controllers and readable by all attached hosts.
Support in SCSI for ‘Supported Behaviors’ of Controllers during failover/failback to meet the needs of different system topologies and operations

## Slide 16
Options for Standardization
Addition of Mode Page definition(s) in the Standard Controller Commands document.
  To ‘register’ all controllers in a fault tolerant configuration as well as LUNs being served by each controller
  TO ‘register’ behavior or controllers during failover/failback
Additional ASC/ASCQ’s for Failover/Failback Events

## Slide 17
Options for Standardization
A combination of a new SCC mode page and additons to the Exception handling page(s) in SCSI-3.
Inquiry data additions for Controllers to give the ‘registration’ information (yuk).

## Slide 18
Conclusions
Controllers in Fault Tolerant Configurations are becoming widespread
Many solutions to support for these configurations exist
Standardization would generalize the problem and solution as well as give Operating Systems MUCH more control and visibility of attached storage subsystems.