## Slide 1
Steve Sicola Digital Equipment Corporation
Proposed Controller Failover Profile

## Slide 2
Proposed Controller Failover Profile
Overview
  Purpose
  Assumptions about Fault Tolerant Controller Configurations & Failover
  Functional Description of FT Controller Configuration Usage
  Additional SCSI-3 Requirements & Issues
  Other High Availability Issues - Hagerman

## Slide 3
Purpose for Profile
Generalize the concept of fault tolerant controller configurations
  1 controller logically with many ports
Generalize usage of SCC to aid OS driver development across all industry platforms for various fault tolerant configuration types
  standardize setup and/or registration of controllers in FT configuration (with naming independent of serial #’s)
  standardize reporting of failing controller/returning controller events
  one port to n-port controller boards
  any number of controller boards in configuration

## Slide 4
SCC & Fault Tolerant Controller Assumptions
Host Bus/Loop/Fabric/etc..
Host
Host
C1
C2
C3
C4
Assumptions
1. All hosts can access
all controller
2. All controllers share
access to storage
3. All controllers can communicate
with all other controllers in
configuration via shared storage
bus(es) or private comm intrfce
4. LUN0 response exactly the
same from all controllers (ie
1 controller logically with n-host
ports

## Slide 5
Functional Description of FT Controller Usage
SCC used to either create attachments between controllers sharing storage or report attachments
;s