## Slide 1
SPI-2 LVDS Driver Tests

## Slide 2
SPI-2 LVDS Driver Z

## Slide 3
SPI-2 LVDS Waveform

## Slide 4
SPI-2 LVDS Termination

## Slide 5
SPI-2 LVDS Diff Sense

## Slide 6
SPI-2 LVDS Bus

## Slide 7
June 21, 1995 Merrimack MTG
Reviewed the document sections of SPI that will be effected by LVDF SPI.
Studied the Diff Sense issues and set new values
Reviewed common mode issues with each interface
Reviewed the cost objectives of LVDS
Defined the pinning for the based on Single ended, regenerated table done in Harrisburg, but not documented.
Note: FAST-40 single ended would still be a longer distance than ATA. This should be a viable standard.
FAST-40 and FAST-80 will require very low delta stub and capacitance for data, parity, ack and req signals. The additive effect of 7 or 15 devices will exceed the skew budget.
Worked timing issues for FAST-40 and FAST-80, external drivers and receivers can not be used, there is no margin in the skew budget.

## Slide 8
Agreements
A single chip may work for both single ended (Async, 5, 10,20) or LVDS (FAST-40,80)
No SE FAST-40
No SE Signals in FAST-40
Timing OK
Diff sense is define with an autosense feature.
low, (SE) all ground drivers shall be on.
Pin outs OK
Target of 15 pF maximum
Current mode Driver, no Driver output impedance spec.
Terminator bias with current limited, 100 mV at 250 microAmps maximum.
No specified receiver hysteresis.

## Slide 9
LVDS Power Calculations
Transceiver power calculations for a 27 line device at 3.3 Volts + 10%.
Maximum 21 Active Drivers on a 27 line device.
27 Active Receivers
Driver control current 1 mA * 3.6 Volts, 3.6 mW * 21 Lines = 75.6 mW
Driver power 4 mA * (3.6-.24) Volts, 13.6 mW * 21 Lines = 285.6 mW
Receiver Power 2.5 mA * 3.6 Volts, 9 mW * 27 Lines = 243 mW
Total Transceiver current 604.2 mW

## Slide 10
LVDS - 6 mA Power
Transceiver power calculations for a 27 line device at 3.3 Volts + 10%.
Maximum 21 Active Drivers on a 27 line device.
6 Active Receivers
Driver control current 1 mA * 3.6 Volts, 3.6 mW * 21 Lines = 75.6 mW
Driver power 6 mA * (3.6-.36) Volts, 19.44 mW * 21 Lines = 408.24 mW
Receiver Power 2.5 mA * 3.6 Volts, 9 mW * 6 Lines = 54 mW
Total Transceiver current 537.84 mW