## Slide 1
SPI-2 - LVDS Meetings
Meetings
Oct 13 Denver SPI-2/LVDS
Oct 16 Milpitas Marketing
Nov 6 Palm Springs

## Slide 2
SPI-2 LVDS Specifications
Oct 13 Meeting
  Adjustment of the drive and thresholds because of the 1/2 current issues of a multipoint busthat was missed in the Bedford, NH Meeting.
    Drive current 4.4 to 6 mA
    Receiver threshold 70 mV
    Terminator bias reduced 100-130 mV
  Symbios Logic Presentation, Hybrid does not work, crosstalk data shows this clearly.
  Bill Ham’s Testing
    100 Megatransfer good at 27 Meters point to point.
    200 Megatransfer the distance will have to be reduced 15 meters?

## Slide 3
Oct 16 SPI-2 Marketing Meeting
Marketing committee will be formed.
  Companies that will be key members: IBM, Digital, Adaptec, Symbios, Qlogic, Quantum, Seagate, Unitrode, Dallas Semi
Function
  Functions
  Dues
  Meetings
  FAX-Back / BBS / Webpage
  Email Reflector / 800#
  Trade Shows
  Publications
  Training
  Press Releases

## Slide 4
SCSI Parallel Marketing
Mission Statement
  Promote increased usage of parallel SCSI
  Educate customers on when to use SCSI
  Reduce confusion concerning SCSI
  Provide focal point for press, industry, and customer communications regarding SCSI
  Advance and promote product interoperability
  Advance and promote storage as a focal point for system differentiation
  Shape the evolution of SCSI technology
  Evangelize SCSI as a flexible and powerful connectivity solution for many applications
  Orchestrate a convergence on a common interconnect

## Slide 5
Nov 6 SPI-2 Meeting
Limiting pin countHybrid discussion came up again, hybrid does not work, this will push some of the controllers to 244 BGA packages. Crosstalk, Common Mode
Definition of the test circuits
  Terminators, Drivers and Device Capacitance
Margin issues
  Suggestion to increase the minimum current to 5 mA
  Reduce the termination impedance to better match the loaded cable, which will guarantee incident wave switching.
  Reduction of Common mode from +/- 1 Volt to +/- 500 mV
  Step getting off the bus, Negate, 1/2 Current, off

## Slide 6
Future Meetings
SPI-2 LVDS
  Dec 15th Holiday Inn Milpitas
  Jan 8th Dallas
  Feb 5th?
SCSI Marketing
  Dec 14th Holiday Inn Milpitas

## Slide 7
LVDS - 6 mA Power
Transceiver Power Calculations
Maximum number of drivers active 23, on 27 line interface.
4 Receivers Active
Driver Control current 1 mA * 3.6 mW * 23 lines = 97.2 mW
Driver power 6 mA * (3.6-0.36) Volts, 19.44 mW/Line * 23 Lines = 447.1 mW
Receiver Power 2.5 mA * 3.6 Volts, 9 mW/Line * 4 Lines = 36 mW
Total Transceiver power = 580 mW
9-Nov-95 Correction