## Slide 1
High Availability Study Group X3T10: 95-312r0
Proposed Controller Failover Profile

## Slide 2
Proposed Controller Failover Profile
Overview
  Purpose
  Architectural Concepts
  The Problem
  Assumptions about Fault Tolerant Controller Configurations & Failover
    Required Changes for SCC & SCSI-3
  Functional Description of FT Controller Configuration Usage
  Additional SCSI-3 Requirements for more Flexibility

## Slide 3
Purpose for Profile
Generalize the concept of fault tolerant controller configurations
  1 controller logically with many ports
Generalize usage of SCC to aid OS driver development across all industry platforms for various fault tolerant configuration types
  standardize setup and/or registration of controllers in FT configuration (with naming independent of serial #’s)
  standardize reporting of failing controller/returning controller events
  one port to n-port controller boards
  any number of controller boards in configuration

## Slide 4
Architectural Concepts
FT Controller Configuration definition:
  Any two or more control units sharing access paths to an arbitrary set of devices/Luns
  Control Units may be active simultaneously or in some kind of active-standby mode
  Differing LUN Access models for hosts

## Slide 5
Architectural Concepts
FT Controller Configuration Definition:
  Failover between controllers
  Failback between controllers
  Failover/Failback by controllers automatically or under host control
  Failover Failback notification direct or indirect (message or timeout)

## Slide 6
The Problem
Non-standard Configuration setup and reporting
Non-standard failover/failback detections & options for speed/simplicity
Interoperability with different OS burdened
Need for standard in open system networked storage environment

## Slide 7
Assumptions & Changes
Assumptions are for adherence to SCC models of SACL’s
Assumptions are:
  Two or more controllers sharing access paths to storage devices
  The controllers configured with devices logically represent ‘one controller with n ports to host’
  The controllers configured with devices report the same configuration between them

## Slide 8
Assumptions and Changes
Assumptions cont;
  Controller communicate with eachother directly (comm) or indirectly (through shared storage) or
  Controller components may have single or multiple host ports & single or multiple device interfaces
  Controllers may be pre-configured or be configured by hosts. Configs verified during controller/host init as well as after initial config
  Any/all surviving controllers within configuration can resume service of storage to host after controller failure.

## Slide 9
SCC & Fault Tolerant Controller Assumptions
Host Bus/Loop/Fabric/etc..
Host
Host
C1
C2
C3
C4
Assumptions
1. All hosts can access
all controller
2. All controllers share
access pathts to storage
3. All controllers can communicate
with all other controllers in
configuration via shared storage
bus(es) or private comm intrfce

## Slide 10
SCC & SCSI-3 Changes
SCC changes involve some specific changes to the ATTACH to COMPONENT DEVICE and REPORT COMPONENT DEVICE ATTACHMENTS service actions
  Changes to Attach involve LUN_C=0 denoting service action for controller attachments
    Changes to parameter list based on LUN_C=0 for list to refer to controllers to be attached to controller receiving service action.

## Slide 11
SCC & SCSI-3 Changes
  Changes to the Report COMPONENT DEVICE ATTACHMENT command
    LUN_C=0 denotes controller service action to report about controller attachments
    Response contains information about all current attachments, the name of the attachment, and information controllers eligible to become attached.

## Slide 12
SCSI-3 Changes
New ASC/ASCq’s for Fault Detection in FT controller configuration:
  FAILOVER
  FAILBACK
  sent to hosts by detecting controller(s) of failed controller. Method determined by SCSI-3 exception handling methods (AEN, Unit Attention, etc..)

## Slide 13
FT Controller Configurations
Using these changes, hosts can
  Configure fault tolerant controller configurations
  Efficient configuration checks by hosts (top level controller checks, followed by One scan down through a controller to verify LUN/device configuration
  Failover/Failback much more quickly since controllers can detect partner failures faster
  Identification of Load balancing opportunities
  Consistent and Complimentary to Persistent Reserve & Global device/LUN IDs

## Slide 14
Additional SCC Requirements for Configuration Flexibility
For more Flexible Configuration, controller configuration capabilities to support multiple configurations of LUNs between attached controllers is possible/desireable
  With networked storage
  With serial storage & high connectivity
Capabilities should be reported and controllable

## Slide 15
Fault Tolerant Configurations
‘N’ Controller component configurations may want/need different LUN access models.
  Total sharing of all LUNs configured between all controllers attached to eachother.
    This is represented by the profile as it stands today with the proposed SCC changes
    This ties a set of controllers to all LUNs configured from any/all controllers in the attached configuration. Class 1 configuration
    Other devices may share access but comprise LUNs for different controller attachments.

## Slide 16
Fault Tolerant Configurations
The Controller Attachment and Controller to LUN attachments allow for
  Ease of configuration: less OS polling of all targets and LUNs to build configuration maps with one or two level controller configurations
    class 1 configuration (one level)
    class 2 configuration (two level)

## Slide 17
Fault Tolerant Configurations
Controller Attachments and Controller to LUN Attachments also provide for
  Easier use and management of Global IDs for devices and LUNs within a controller configuration.

## Slide 18
Fault Tolerant Configurations
LUNs attached to specific sets of controllers within an attached controller configuration
    This requires an Attachment of Controller to specific LUN. It also implies a set of flags for reporting of and control of the LUN access method to be employed by the controller(s) attached to the LUN.

## Slide 19
Fault Tolerant Configuations
The LUN attachment method is basically a ‘Sub-component attachment between controllers to sets of LUNs on shared access paths. Class 2 configuration.
  A Create Controller-LUN Attachment command would need to be added
    Global ID Assignment
    Setup Class of LUN Service

## Slide 20
LUN Access/Service Methods
LUN access with controllers may be:
  Allowed by only one controller, that controller only responds to read/write commands
  Allowed by one controller at a time, but requires interlock commands to bind/unbind from a controller (i.e. Reserve/Release)
  Allowed by both controller simultaneously, assuming a high level of interlock on LUN accesses

## Slide 21
Fault Tolerant Configurations
A Report Controller-LUN Attachment Command will also be required
    To Report Attached LUNs
    To Report Eligible LUNs
The Report Component Device Attachment (for Controllers, LUN_C=0) needs
  To Report Class of LUN access/service Allowed
  Controller Configuration Type (1,2,other)