## Slide 1
LVD SCSI Assertion and Negation Currents
Richard S. Moore
Adaptec

## Slide 2
Purpose
Define an operating region for driver assertion and negation currents (IA and IN) that will provide adequate DC voltage levels, incident wave voltage levels, and reflected wave voltage levels. IA and IN are defined such that both are positive quantities.

## Slide 3
Constraints
DC voltage levels:
  VA >= 130 mV
  VN <= -130 mV
AC voltage levels (first transition):
  V+ >= 150 mV
  V- <= -150 mV
Cable impedance:
  85 ohms <= ZL <= 135 ohms

## Slide 4
Constraints (continued)
Termination:
  100 mV <= VB <= 130 mV
  100 ohms <= RT <= 115 ohms
  0.87 mA <= IT <= 1.3 mA (derived)
Leakage and number of nodes:
  -20 uA <= IL <= 20 uA
  2 <= N <= 16

## Slide 5
DC Assertion Level
VA >= 130 mV
(IA - 2 * IT - N * IL) * RT / 2 >= 130 mV
IA >= 2 * (130 mV + VB) / RT + N * IL
Maximum VB, N, and IL; minimum RT:
IA >= 5.52 mA

## Slide 6
DC Negation Level
VN <= -130 mV
-(IN + 2 * IT + N * IL) * RT / 2 <= -130 mV
IN >= 2 * (130 mV - VB) / RT - N * IL
Minimum VB, IL, and RT; maximum N:
IN >= 0.92 mA

## Slide 7
Incident Wave Assertion
V+ >= 150 mV
VN + (IA + IN) * ZL / 2 >= 150 mV
IA + IN >=
(300 mV + (IN + 2 * IT + N * IL) * RT) / ZL

## Slide 8
Incident Wave Assertion (cont.)
IA >=
300 mV + IN * (RT - ZL) + 2 * VB + N * IL * RT
ZL
Maximum RT, minimum ZL:
IA >= 7.02 mA + .35 * IN

## Slide 9
Reflected Wave Assertion
VR+ >= 130 mV
Let ZP = RT * ZL / (RT + ZL)
VN + (IA + IN) * ZP >= 130 mV
IA + IN >=
(130 mV + (IN + 2 * IT + N * IL) * RT / 2 ) / ZP

## Slide 10
Reflected Wave Assertion (cont.)
IA >=
130 mV + IN * (RT/2 - ZP) + VB + N * IL * RT/2
ZP
Minimum RT and ZL:
IA >= 6.01 mA + .09 * IN
Maximum RT, minimum ZL:
IA >= 5.69 mA + .18 * IN

## Slide 11
Reflected Wave Assertion (cont.)
Superposition of both reflected waves -- let ZR = 2 * ZP - ZL / 2
IA >=
130 mV + IN * (RT/2 - ZR) + VB + N * IL * RT/2
ZR
Maximum ZL, minimum RT:
IA >= 5.83 mA + .055 * IN

## Slide 12
Incident Wave Negation
V- <= -150 mV
VA - (IA + IN) * ZL / 2 <= -150 mV
IA + IN >=
((IA - 2 * IT - N * IL) * RT + 300 mV) / ZL

## Slide 13
Incident Wave Negation (cont.)
IN >=
IA * (RT - ZL) - 2 * VB - N * IL * RT + 300 mV
ZL
Minimum ZL, maximum RT:
IN >= 1.61 mA + .35 * IA

## Slide 14
Reflected Wave Negation
VR- <= -130 mV
VA - (IA + IN) * ZP <= -130 mV
IA + IN >=
((IA - 2 * IT - N * IL) * RT / 2 + 130 mV) / ZP

## Slide 15
Reflected Wave Negation (cont.)
IN >=
IA * (RT/2 - ZP) - VB - N * IL * RT / 2 + 130 mV
ZP
Minimum ZL, maximum RT:
IN >= 0.99 mA + .18 * IA

## Slide 16
Reflected Wave Negation (cont.)
Superposition of both reflected waves
IN >=
IA * (RT/2 - ZR) - VB - N * IL * RT / 2 + 130 mV
ZR
Minimum RT, maximum ZL:
IN >= 0.97 mA + .055 * IA

## Slide 17
Ideal Asymmetric Drivers
VA = - VN
(IA - 2 * IT) * RT / 2 = (IN + 2 * IT) * RT / 2
IA = IN + 4 * IT
IT (mid-range) = 1.05 mA
IA = IN + 4.2 mA

## Slide 18
Symmetric and Asymmetric Drive
Symmetric drivers with 10% mismatch:
IA >= 0.9 * IN
Asymmetric drivers with 10% mismatch:
IA <= 1.1 * IN + 4.6 mA

## Slide 19
Allowed Region of Operation
Recommended bound
for asymmetric drivers
Recommended bound
for symmetric drivers

## Slide 20
Comments
Analysis is for current-mode drivers and neglects driver and load impedances; i.e., RS >> ZL and RL >> ZL.
A simple current source model for leakage is used. A better model would be a diode bridge with a current source.

## Slide 21
Comments
Worst case conditions arise from lowest loaded cable impedance combined with highest termination resistance.
Incident wave amplitude is the dominant constraint for both assertion and negation drivers.

## Slide 22
Comments
Tightening range of RT would provide relief by relaxing driver design constraints.
If minimum negation current for DC conditions is positive, does this mean that the terminator bias is insufficient?