## Slide 1
LVD SCSI Driver Proposal
Richard S. Moore
Adaptec

## Slide 2
Existing Boundaries
Test circuit (SPI-2 10.1.1):
9.7 mA < Ia < 15.0 mA
4.9 mA < In < 15.8 mA
-0.9 mA < Ia - In < 7.5 mA
This describes a diagonal band across a rectangular region.
Algebraically derived minimum requirements:
Ia >= 7.02 mA + .353 * In
In >= 1.61 mA + .353 * Ia
This describes a wedge-shaped region.

## Slide 3
SPI-2 Test Circuit (10.1.1)

## Slide 4
Algebraic Solution

## Slide 5
Overlay of Both Regions
A
B
C
D
E

## Slide 6
Points of Interest
Label In (mA) Ia (mA) Significance
A 4.7 8.7 Tip of wedge
B 7.6 9.7 Intersection of wedge and bottom edge of rectangle
C 15.8 9.7 Lower right-hand corner of rectangle
D 15.8 15.0 Upper right-hand corner of rectangle
E 6.9 15.0 Intersection of wedge and top edge of rectangle
Consider region ABCDE.
Point C fails in Kevin Gingerich’s spreadsheet model. Either move up or move left.
Points B and E are unnecessarily strict. Eliminate B and move E to the left.

## Slide 7
Points of Interest
Label In (mA) Ia (mA) Significance
A 4.7 8.7 Tip of wedge
C' 10.1 9.7 Rightmost working point on bottom edge of rectangle
C’’ 15.8 10.8 Lowest working point on right-hand edge of rectangle
D 15.8 15.0 Upper right-hand corner of rectangle
E' 4.8 15.0 Leftmost working point on top edge of rectangle
Consider AC’DE’. Boundary includes 3 diagonals and one horizontal segment.
AC’’DE’ requires one less diagonal segment and is therefore easier to specify.
The spreadsheet model shows that all four corners of AC’DE’ or AC’’DE’ give sufficient assertion-to-negation and negation-to-assertion transitions under worst case conditions.

## Slide 8
Modified Region of Operation
A
C’’
D
E’

## Slide 9
Objection: 4:1 Voltage Ratio
Need to meet receiver input balance requirements.
Derive an additional boundary condition:
|VN| <= 4*|V+|
-VN <= 4*(VN + (IA + IN)*ZL/2)
5* VN + 2*(IA + IN)*ZL >= 0
5*(IN*RT/2 + VB) <= 2*(IA + IN)*ZL
IA >= 3.8 mA + .69*IN
Similar derivation to ensure |VA| <= 4*|V-| gives:
IN >= -2.9 mA + .69*IA
or,
IA <= 4.2 mA + 1.45*IN

## Slide 10
Revised Region of Operation

## Slide 11
New Boundaries
IA >= 7.8 mA + 0.19 * IN (AC’’)
IN <= 15.8 mA (C’’D)
IA <= 15.0 mA (DE’)
IN >= 4.5 mA + 0.02 * IA (E’A)
IA >= 3.8 mA + 0.69 * IN (receiver
IN >= -2.9 mA + 0.69 * IA balance)

## Slide 12
Proposed Test Conditions
Replace:
416 mV <= VA <= 706 mV
with:
309 mV + 0.19 * |VN| <= VA <= 706 mV
Replace:
381 mV <= |VN| <= 977 mV
with:
361 mV + 0.02 * VA <= |VN| <= 977 mV
Replace:
-277 mV < |VA| - |VN| < 181 mV
with:
91 mV + 0.69 * |VN| <= VA <= 113 mV + 1.45 * |VN|

## Slide 13
Further Improvements?
Lowering the maximum termination resistance or the maximum bias voltage reduces the drive current requirement by about 0.5 to 1.0 mA. Minimum values for these parameters should not be changed.
How much tightening of these parameters (if any) can be tolerated by terminator designers?