## Slide 1
Proposal for Additional Persistent Reservation Functions
SCSI Working Group
Natick, MA
September 9-10, 1996
Tom Coughlan
Digital Equipment Corporation

## Slide 2
Multiple-Initiator Systems
Multiple SCSI initiators must use some form of coordination when accessing shared storage devices.
It is desirable for one or more initiators to take over when an initiator becomes unresponsive:
initiator
initiator
initiator
initiator
initiator
Host
Host
Host
task set
Device
Server
SCSI
coordination mechanism

## Slide 3
Recovery From Unresponsive Initiator(s)
The survivors must determine that:
  there are no tasks from the unresponsive initiator in the device server
    and no ACA conditions
  there are no reservations for the unresponsive initiator
  no further tasks from the non-responsive initiator will be accepted
initiator
initiator
initiator
initiator
initiator
Host
Host
Host
task set
Device
Server
SCSI
coordination mechanism

## Slide 4
Constraints
Recovery should be fast, since access to the shared resource is blocked until it completes.
Recovery should not disrupt any tasks that the survivors have already queued to the device.

## Slide 5
The Current Solution
A survivor can issue a Preempt and Clear, with an Exclusive reservation.
  this removes the appropriate tasks and reservations from the device server, clears ACA, and blocks subsequent tasks
  unfortunately, it also blocks access by all the other initiators in the system
A Shared Access reservation would allow multi-access, but then the unresponsive initiator’s in-flight commands would not be blocked.

## Slide 6
The Proposal
Add a new Persistent Reservation Type, called “Shared Access, Registrants Only”
  allows Read, Write, and Reserve, but only for registered initiators
  does not conflict with itself
Locking out non-registered initiators is a Good Thing
  they are clearly not cooperating

## Slide 7
An Example Application
When a Host boots each initiator:
  Registers
  Issues a Shared Access, Registrants Only Reservation
When an host becomes unresponsive, one or more of the survivors:
  Issue a Persistent Reservation
    Action = Preempt and Clear
    Type = Shared Access, Registrants Only
    Service Action Key = the key of the unresponsive initiator
When a Host recovers, it:
  Ensures all of its old commands are flushed.
  Re-registers and re-reserves.

## Slide 8
Summary
One change is required to support simultaneous access multiple initiator systems.
The initial proposal, posted to the SCSI reflector, called for an additional change, so that Preempt and Clear could be applied to all non-registered initiators.
  the goal was to provide a means to Preempt a set of nodes quickly, and without haveing to learn each one’s key
  this has been reconsidered, and is not being proposed at this time.