## Slide 1
Do Read Long and Write Long have a Secure Future? ( Was: A proposal to add a new modifier to SCSI Write commands )
Tom Coughlan
Digital Equipment Corporation
January 8, 1997

## Slide 2
Read and Write Long Applications
To force an unrecovered read error
  useful for disk mirroring applications
To test the error detection and correction mechanisms in the storage device

## Slide 3
Read and Write Long Disadvantages
Write Long is not an ideal mechanism for creating forced errors:
  the length is drive-specific
  the data pattern is theoretically drive-specific
Write Long can be used by malicious utilities to make a drive appear bad.

## Slide 4
An Alternative
Add a bit to the Write commands that would instruct the drive to return an unrecovered ECC error on subsequent reads.
  Only one-block transfer lengths allowed.
  Subsequent writes with the "force error" bit clear would return the block to normal status.
Advantages:
  provides a vendor-independent method for creating forced errors
  ( does not infringe on DIGITAL’s patent )

## Slide 5
Reactions
Strong sentiment in favor of keeping Read and Write Long
  they are used as a test tool
Preference for avoiding an additional way to do the same thing
  the new Write bit is probably not worth adding unless R/W Long are obsoleted
Some interest in extending the new Write functionality:
  generate a unique error when read
  Read returns the data that was written
  additional Write modifier bits, each with unique Read error codes

## Slide 6
Resolution
Write Long is adequate for writing forced errors, if it will remain in the Standard, and in common implementations.
Strong desire to keep R/W Long as a testing tool, indicates that it will not be obsoleted.
  right?
In light of this, the additional mechanism for writing forced errors is not justified.
  No further work on the proposal is planned.